## Slide 1: MA-Project “System Structure and Parameterization” – Early Insights
presented by Jochen Köhler (ZF)
Japanese Modelica Conference 2016-05-23/24
Tokyo / Japan
J. Köhler
P. R. Mai
J. Krasser
M. Nagasawa
M. Deppe

## Slide 2: Motivation for initiating MAP “System Structure and Parameterization” (SSP) – Using FMI as Basis
FMI is basically a great technology to make exchanging models inside and among companies much easier
Typical use-case is a network of FMUs (System structure) …
… Therefore, some features are missing …

## Slide 3: Motivation for initiating SSP – Missing features
Collected on a meeting with BMW, Bosch, ZF, PMSF (2014):
  No possibility to separate parameter data from the FMUs
  No possibility to change parameters in a consistent way independently from the integration environment for single FMUs.
  No possibility to handle intellectual property of parameters
  No possibility of mapping parameters in a network of FMUS
  No possibility to store a network of FMUs tool independently

## Slide 4: Main Purposes of SSP
Define a standardized format for the connection structure of a network of components.
Define a standardized way to store and apply parameters to these components.
The developed standard / APIs should be usable in all stages of development process (architecture definition, integration, simulation, test in MiL, SiL, HiL).
The work in this project shall be coordinated with other standards and organizations (FMI, ASAM, OMG).
Notes: ASAM (Association for Standardization of Automation and Measuring Systems) is an incorporated association under German law. Our members are primarily international car manufacturers, suppliers and engineering service providers from the automotive industry.
ASAM coordinates the development of technical standards, which are developed by working groups composed of experts from our member companies. We pursue the vision that the tools of a development process chain can be freely interconnected and allow a seamless exchange of data.
The Object Management Group® (OMG®) is an international, open membership, not-for-profit technology standards consortium, founded in 1989. OMG standards are driven by vendors, end-users, academic institutions and government agencies. OMG Task Forces develop enterprise integration standards for a wide range of technologies and an even wider range of industries. OMG’s modeling standards, including the Unified Modeling Language® (UML®) and Model Driven Architecture® (MDA®), enable powerful visual design, execution and maintenance of software and other processes

## Slide 5: Overview of XML Schema Definitions
Par2
Par1
Par…
*.SSV
SSD
System
Element
name :string
Compo
nent
source :URI
type :string
Connector
name :string
kind :enum
Connection
suppressUnitConversion :boolean
System
Structure
Definition
Parameter
Binding
source :URI
type :string
Parameter
Mapping
source :URI
type :string
SignalDictio
nary
Reference
Signal
Dictio
nary
0..*
ParameterMappings
0..*
ParameterBindings
0..*
end
1
1
0..*
Connections
0..*
Connectors
0..*
Elements
0..*
start
1
0..*
SignalDictionaries
1
0..*
*.FMU
SSD
FMU
SSP
*.SSP
Map1
Map2
Trans
*.SSM
Notes: Four Defined Formats:
  SSD for Structure
  FMU as fundamental Building Block
  SSV for Param Values
  SSM for Param Bindings
  SSP for Packaging/Variant-Handling

## Slide 6: XML Schema Description - System Structure Package
Use case
Exchange of Complete Systems with Variants
Features
All information (FMUs, system structure definition, parameters) can be stored in one archive (zip-file)
Multiple SSDs in one SSP allows for variant modeling
SSD
FMU
SSP
*.SSP

## Slide 7: XML Schema Description - System Structure Definition
Use case
Defining a Network of FMUs
Features
Hierarchical sub-systems
Empty components/FMUs as interface templates
External resources via URIs: Both relative to SSD/SSP or absolute, e.g. via HTTP(S).
Connections with unit conversions and optional linear/map transformations
Optional: Diagram geometry
SSD
System
Element
name :string
Compo
nent
source :URI
type :string
Connector
name :string
kind :enum
Connection
suppressUnitConversion :boolean
System
Structure
Definition
Parameter
Binding
source :URI
type :string
Parameter
Mapping
source :URI
type :string
SignalDictio
nary
Reference
Signal
Dictio
nary
0..*
ParameterMappings
0..*
ParameterBindings
0..*
end
1
1
0..*
Connections
0..*
Connectors
0..*
Elements
0..*
start
1
0..*
SignalDictionaries
1
0..*

## Slide 8: XML Schema Description - System Structure Definition
Notes: System consists of Elements (Component, SignalDictionaryReference, System), Connections and optional SignalDictionaries and Geometry Information
Elements all contain Connectors and optional ParameterBindings and Geometry Information
Components are atomic elements, they reference FMUs or other SSPs/SSDs
Components could also support other modeling entities, like Modelica Models, …

## Slide 9: XML Schema Description - Signal dictionaries
Use cases
Collecting Control Signals in a Central Location
Features
Causality is checked by tool automatically
Crosses hierarchies without need for downward passing
Well-suited for e.g. ECU control busses
Notes: SignalDictionaries define the actual signals in the dictionary
SignalDictionaryReferences at the same or lower hierarchy levels can directly reference those, crossing intermediate levels without notice

## Slide 10: XML Schema Description – Parameter Values Data
Use case
Tool-independent Exchange of Parameter Data
Features
Neutral exchange format between parameter sources
Compatible to FMI standard
Provides some meta data
Access to param DBs via HTTP (-> Parameter API)
SSV
ParameterSet
+
name :string
Parameter
+
name :string
Unit
+
name :string
BaseUnit
+
kg :int
+
m :int
+
s :int
+
A :int
+
K :int
+
mol :int
+
cd :int
+
rad :int
«choice»
Type
Real
+
value :double
Integer
+
value :int
Enumeration
+
value :string
Boolean
+
value :boolean
String
+
value :string
Annotation
+
type :string
+
body :XML
unit
0..*
Units
0..*
Parameters
0..*
Annotations
0..*
Annotations
Notes: Simple Format, Easy to use as a lingua franca
Same Format used to access sources via Parameter Get API, can be used for Parameter DBs or Parameter Converters from other formats (e.g. ASAM MCD -> SSV)

## Slide 11: XML Schema Description - Parameter Mapping
Use case
Mapping Parameters to FMUs when the Parameter Names differ or Parameter Values require Transformations
Features
Can be stored separately from System Structure and Parameter Data
Can be inlined into SSD
Optional manual linear and mapping transformations
SSM
Parameter
Mapping
MappingEntry
+
source :string
+
target :string
+
suppressUnitConversion :boolean
Transfor-
mation
Linear
Transformation
+
factor :double
+
offset :double
IntegerMapping
Transformation
MapEntry
+
source :int
+
target :int
EnumerationMapping
Transformation
MapEntry
+
source :string
+
target :string
1..*
1..*
0..1
0..*
Notes: - Only needed when names differ (other than prefixes) or transformations other than automatic unit conversions are needed and SSV source shall remain unchanged.

## Slide 12: Parameter API Get Mechanisms
General Idea:
  Access to external parameter sources via HTTP(S) GET Requests
  Request URI is the source attribute
  Type attribute passed via accept request header
  Updates handled efficiently via ETag/Conditional GET/HEAD
Returns Parameter Data in the format requested:
  application/x-ssp-parameter-set -> SSV file format
  Sources and tools can support other formats
Data Source
Authoring Tool
ParamSet
Editing Parameters directly
Model
P1 P2 P3
Editing Assignments with direct access to parameters
HTTP GET Requests

## Slide 13: Parameter API Get Mechanisms
GET /context/ParamSetA HTTP/1.1
Host: pardb.example.com:80
Accept: application/x-ssp-parameter-set
HTTP/1.1 200 Ok
Content-Type: application/x-ssp-parameter-set
Content-Length: …
ETag: "3f80f-1b6-3e1cb03b"
<?xml version="1.0" encoding="UTF-8"?> <ssv:ParameterSet version="Draft20151124" name="SystemParams" …>
<ssv:Parameters>
…
Future extension:
  Request version/ variant Descriptor for Resources
  Query for alternative versions/ variants based on descriptor with wild-cards
  Full parameter management API for editing, managing parameters and parameter Sets

## Slide 14: Integration of FMUs for HIL Testing
HIL configuration tools are importing FMUs to integrate them with other FMUs, Simulink-based models and real ECUs
Data Management tools are managing the lifecycle of the FMUs
Model B
Model A
Export
Import
Model Management
HIL Configuration
HIL Integration
Modeling
Data Management
Notes: FMUs are imported into HIL configuration tools to integrate them with other FMUs, Simulink-based models, Virtual-ECUs or real ECUs
Data Management environments import the FMU metadata (incl. interfaces) and allow consistent version control of the metadata and the FMU container file to manage the lifecycle of the FMUs.

## Slide 15: Reuse of the System Structure for SIL, MIL and HIL
Integration and Data Management tools share a vendor independent system description (SSP)
Reuse of tools, configurations, models, tests, layouts and parameters at system level is supported
HIL Integration
Model Management
HIL Configuration
Integration
Data Management
*.SSP
SSD
FMU
SSP
Configuration Offline Simulation
Notes: There is an increasing desire to reuse environment models to provide proven, consistent solutions for the validation of controller models in different projects and development stages (e.g., for virtual validation and HIL simulations).
Data Management environments provide capabilities for managing model compositions, handling variants of systems and managing the parameter and signal interfaces of the different model systems.
The SSP approach allows to share a standardized system structure description between data management, integration and configuration tools for SIL, MIL and HIL scenarios

## Slide 16: Prototypes – Integration Tool
Model.CONNECTTM by AVL – Scope:
  Simulation architecture set-up
  Model integration (FMI and dedicated interfaces)
  Execution (office and lab)
  Model management
  Handling system structure and parameter variants

## Slide 17: Prototypes – Integration Tool
Model.CONNECTTM by AVL – SSP prototype:
  Import and export of system structure (SSP packages)
    Prototype supports multiple structure variants in the package
    Mapping between the SSP variant handling and the tool-specific variant handling had to be implemented
    Import-export roundtrip does not re-produce original ssp content
    This is a consequence of the deliberately simple SSP variant handling concept
  Import and export of graphical information
    Overall layout information can be transferred via SSP. Intention is not to have pixel-by-pixel reproduction in any tool

## Slide 18: Prototypes: Integration Tool FMI Bench
FMI Bench by PMSF: Workbench for FMUs
  FMU Inspector & Editor
  FMU Profiling and Debugging
  FMU Integration
  Automated Workflows
  Export FMU Networks as Integrated FMUs or Stand-alone Simulators
  Supports Remote FMU Execution, FMU-internal Parallelization

## Slide 19: Prototypes: Integration Tool FMI Bench
FMI Bench SSP Prototype
  Direct Editing of SSDs, SSPs, incl. Variants
  Generation of Native FMI Bench Projects from SSP Projects
  Generation of FMU or Stand-alone Sim. from SSP
  Parallelization

## Slide 20: Prototypes – Online Testing Tool
Scalablility of <ssd:Connectors>
  Ring configuration at a glance
  3D Flash UI for <ssd:Component>
Time integration control master
  Unit Test with default parameter
  Synchronized Co-Simulation Test
Parameter database as FMU
  FMU of (sqlite.DB + sql.DLL)
  exported by Optimus®
Notes: In the SSP project, we define three-tool category: Authoring tool, Integration tool, and Simulation tool.
This prototype (by Cybernet Japan) is a light-weight simulation tool
suitable for "Online Testing Environment" among multi-organizational users.
The merit of open Standard is to connect people, engineers and users freely and INTERNATIONALLY!
Design of Co-simulation experiments would be easier, as FMI and SSP standards are getting popular.
Even a small Database such as “sqlite” and its IO library can be included as a single FMU,
compatible with FMI standard, in our SSP platform paradigm.

## Slide 21: Prototypes – “Co-Simulation Browser” concept
Mobile co-Simulation environment
SSP(.zip) as online content
Minimal GUI
Notes: Another merit of SSP is to accelerate the multi-user collaborations among OEM and suppliers, with multi-domain expertise.
As Internet Browser of HTML content opened the new world of Information Distribution,
SSP would be able to enlarge the Model Distribution World.
The concept of "Co-Simulation browser of SSP package" would be useful to explain the
future roles and possibilities of SSP to increase the popularities of Co-Simulations
among younger generations who are accustomed with Smart device operations.
The Cybernet R&D prototype is in pursuit of this direction of Smart User Interface.

## Slide 22: Future work / Outline
Further Development of API for parameter handling
Try to involve providers of simulation data management systems in this project
Evaluate approaches with „real-world examples“
Publish first release soon
Any contribution is very appreciated!

## Slide 23: XML Schema Description - System Structure Definition
Notes: Show Parameter Bindings at System and at Component Level
SignalDictionaryReference, Connectors, Connections
SignalDictionaryReferences are analogue to instances of SignalDictionaries where you can specifiy also causality of connectors