## Slide 1: MA-Project “System Structure and Parameterization” – Current Status and Plans
presented by Jochen Köhler (ZF), Pierre R. Mai (PMSF)
FMI User Meeting 2017-05-15
Prague / Czech Republic
J. Köhler
P. R. Mai
J. Krasser
M. Nagasawa
M. Deppe
Modelon Logo
M. Henningsson
TLK Thermo
J.N. Jäschke
T. Sommer
M. Najafi

## Slide 2: Main Purposes of SSP – Based on FMI standard
Define a standardized format for the connection structure of a network of components (FMUs in particular).
Define a standardized way to store and apply parameters to these components.
The developed standard / APIs should be usable in all stages of development process (architecture definition, integration, simulation, test in MiL, SiL, HiL).
The work in this project shall be coordinated with other standards and organizations (FMI, ASAM, OMG).
Notes: ASAM (Association for Standardization of Automation and Measuring Systems) is an incorporated association under German law. Our members are primarily international car manufacturers, suppliers and engineering service providers from the automotive industry.
ASAM coordinates the development of technical standards, which are developed by working groups composed of experts from our member companies. We pursue the vision that the tools of a development process chain can be freely interconnected and allow a seamless exchange of data.
The Object Management Group® (OMG®) is an international, open membership, not-for-profit technology standards consortium, founded in 1989. OMG standards are driven by vendors, end-users, academic institutions and government agencies. OMG Task Forces develop enterprise integration standards for a wide range of technologies and an even wider range of industries. OMG’s modeling standards, including the Unified Modeling Language® (UML®) and Model Driven Architecture® (MDA®), enable powerful visual design, execution and maintenance of software and other processes

## Slide 3: Overview of File Definitions
Par2
Par1
Par…
*.SSV
SSD
System
Element
name :string
Compo
nent
source :URI
type :string
Connector
name :string
kind :enum
Connection
suppressUnitConversion :boolean
System
Structure
Definition
Parameter
Binding
source :URI
type :string
Parameter
Mapping
source :URI
type :string
Signal Dictionary
Reference
Signal
Dictio
nary
0..*
ParameterMappings
0..*
ParameterBindings
0..*
end
1
1
0..*
Connections
0..*
Connectors
0..*
Elements
0..*
start
1
0..*
SignalDictionaries
1
0..*
*.FMU
SSD
FMU
SSP
*.SSP
Map1
Map2
Trans
*.SSM
Sig2
Sig1
Sig…
*.SSB
Notes: Four Defined Formats:
  SSD for Structure
  FMU as fundamental Building Block
  SSV for Param Values
  SSM for Param Bindings
  SSP for Packaging/Variant-Handling

## Slide 4: List of features
Hierarchical description of systems of connected components
Components: FMUs and external SSPs/SSDs, extensible to models, …
Parameter bindings both at component and system-level, including transformations and name/unit-mapping
Signal dictionaries support cross-hierarchical data pools (e.g for busses)
Packaging of SSDs, FMUs, Parameters, … into one bundle (SSP)
Light-weight support for variant handling at SSP level (multiple SSDs sharing components, parameters, resources)
Optional exchange of graphical information (similar display across tools)
URI references to all resources: Integration with other systems via URIs

## Slide 5: Parameter Handling with Simulation Data Management Systems and Authoring Tools
Results from workshop with SDM vendors:
  Direct connection between SDM and authoring tools is not the preferred way
  Parameter and system structure exchange could be done via file transfer (SSP standard)
  Further measures will be taken to make a proof of concept

## Slide 6: Integration of FMUs for SIL & HIL with SSP: Reuse of the System Structure
The System Structure defined for SIL can be reused for HIL testing
It becomes possible to reuse more models, configurations, tests, layouts and parameters
A Data Management tool controls the lifecycle of the SSP
HIL Integration
Model Management
HIL Configuration
SIL Integration
Data Management
*.SSP
SSD
FMU
SSP
SIL Configuration
Notes: There is an increasing desire to reuse environment models to provide proven, consistent solutions for the validation of controller models in different projects and development stages (e.g., for virtual validation and HIL simulations).
Data Management environments provide capabilities for managing model compositions, handling variants of systems and managing the parameter and signal interfaces of the different model systems.
The SSP approach allows to share a standardized system structure description between data management, integration and configuration tools for SIL, MIL and HIL scenarios

## Slide 7: Potential further work
Components can support more than FMUs/SSPs:
  New ADAS Sensor Interfaces currently in development (Object Lists)
Open Issues in SSP
  Start values for Inputs
    Subsystems / t=0
  Initial state of the system
  Experiment setup
    Start time, stop time, selected results
    Selection of solver, -settings, subsystem handling
  FMU-instance specific settings
    e.g. Sync rate, (Co-)Simulation mode, Import Settings
Reliability check
  Similar to FMI Crosschecks
Notes: Initial / Start values for Inputs needed for initialization
Defining the initial state of the system (eg ModelExchange)
Experiment setup
  Orientate on how Modelica does it
Reliability checks:
  Provide reference results
  Allow the user to validate the SSP after importing

## Slide 8: Existing prototypes with support of SSP
Model.CONNECTTM by AVL – Scope
Integration Tool FMI Bench by PMSF
Co-Simulation Player” (Cybernet)
TLK MoBA Lab by TLK
FMI Composer by Modelon
FMI Kit – FMI Library for Simulink by Dassault
SSP support by solidThinking Activate® by Altair

## Slide 9: Requested Features from FMI
Nice support of vectors / arrays for parameters and signals
Notes: Initial / Start values for Inputs needed for initialization
Defining the initial state of the system (eg ModelExchange)
Experiment setup
  Orientate on how Modelica does it
Reliability checks:
  Provide reference results
  Allow the user to validate the SSP after importing

## Slide 10: Current Roadmap for First Release
Topic | Due Date
Presenting on Modelica Conference | 2017-05-15/17
End of Beta test phase | 2017-09-30
Initiate website | 2017-05-31
Review of existing documents | 2017-05-31
Release Beta version | 2017-06-01
Review of existing documents | 2017-10-14
Release version 1.0 | 2017-11-30

## Slide 11: BACKUP

## Slide 12: File Definitions - System Structure Package (*.SSP)
Use case
Exchange of Complete Systems with Variants
Features
All information (FMUs, system structure definition, parameters) can be stored in one archive (zip-file)
Multiple SSDs in one SSP allows for variant modeling
SSD
FMU
SSP
*.SSP

## Slide 13: File Definitions - System Structure Definition (*.SSD)
Use case
Defining a Network of FMUs
Features
Hierarchical sub-systems
Empty components/FMUs as interface templates
External resources via URIs: Both relative to SSD/SSP or absolute, e.g. via HTTP(S).
Connections with unit conversions and optional linear/map transformations
Optional: Diagram geometry
SSD
System
Element
name :string
Compo
nent
source :URI
type :string
Connector
name :string
kind :enum
Connection
suppressUnitConversion :boolean
System
Structure
Definition
Parameter
Binding
source :URI
type :string
Parameter
Mapping
source :URI
type :string
SignalDictio
nary
Reference
Signal
Dictio
nary
0..*
ParameterMappings
0..*
ParameterBindings
0..*
end
1
1
0..*
Connections
0..*
Connectors
0..*
Elements
0..*
start
1
0..*
SignalDictionaries
1
0..*

## Slide 14: File Definitions - Signal Dictionaries (*.SSB)
Use cases
Collecting Control Signals in a Central Location
Features
Causality is checked by tool automatically
Crosses hierarchies without need for downward passing
Well-suited for e.g. ECU control busses
Can be inline or in external file
Notes: SignalDictionaries define the actual signals in the dictionary
SignalDictionaryReferences at the same or lower hierarchy levels can directly reference those, crossing intermediate levels without notice

## Slide 15: File Definitions – Parameter Values Data (*.SSV)
Use case
Tool-independent Exchange of Parameter Data
Features
Neutral exchange format between parameter sources
Compatible to FMI standard
Provides some meta data
Access to param DBs via HTTP (-> Parameter API)
SSV
ParameterSet
+
name :string
Parameter
+
name :string
Unit
+
name :string
BaseUnit
+
kg :int
+
m :int
+
s :int
+
A :int
+
K :int
+
mol :int
+
cd :int
+
rad :int
«choice»
Type
Real
+
value :double
Integer
+
value :int
Enumeration
+
value :string
Boolean
+
value :boolean
String
+
value :string
Annotation
+
type :string
+
body :XML
unit
0..*
Units
0..*
Parameters
0..*
Annotations
0..*
Annotations
Notes: Simple Format, Easy to use as a lingua franca
Same Format used to access sources via Parameter Get API, can be used for Parameter DBs or Parameter Converters from other formats (e.g. ASAM MCD -> SSV)

## Slide 16: File Definitions - Parameter Mapping (*.SSM)
Use case
Mapping Parameters to FMUs when the Parameter Names differ or Parameter Values require Transformations
Features
Can be stored separately from System Structure and Parameter Data
Can be inlined into SSD
Optional manual linear and mapping transformations
SSM
Parameter
Mapping
MappingEntry
+
source :string
+
target :string
+
suppressUnitConversion :boolean
Transfor-
mation
Linear
Transformation
+
factor :double
+
offset :double
IntegerMapping
Transformation
MapEntry
+
source :int
+
target :int
EnumerationMapping
Transformation
MapEntry
+
source :string
+
target :string
1..*
1..*
0..1
0..*
Notes: - Only needed when names differ (other than prefixes) or transformations other than automatic unit conversions are needed and SSV source shall remain unchanged.

## Slide 17: State of the Art: Integration of FMUs for SIL & HIL
Integration tools are importing FMUs, Simulink-based models and ECU code
A Data Management tool controls the lifecycle of all models
The SIL/HIL integration results (System Descriptions) can not be exchanged easily among the tools
Export
Import
Model Management
SIL/HIL Integration
Data Management
Model B
Model A
Modeling
Notes: FMUs are integrated with other FMUs, Simulink-based models, Virtual-ECUs or real ECUs
Data Management environments import the FMU metadata (incl. interfaces) and allow consistent version control of the metadata and the FMU container file to manage the lifecycle of the FMUs.
The individual integration results (System Descriptions) can not be reused easily in the toolchain. Especially not if the tools are provided by different vendors.
A step-wise transition from the SIL to the HIL test is time consuming.

## Slide 18: Prototypes – Integration Tool
Model.CONNECTTM by AVL – Scope:
  Simulation architecture set-up
  Model integration (FMI and dedicated interfaces)
  Execution (office and lab)
  Model management
  Handling system structure and parameter variants
OLD

## Slide 19: Prototypes – Integration Tool
Model.CONNECTTM by AVL – SSP prototype:
  Import and export of system structure (SSP packages)
    Prototype supports multiple structure variants in the package
    Mapping between the SSP variant handling and the tool-specific variant handling had to be implemented
    Import-export roundtrip does not re-produce original ssp content
    This is a consequence of the deliberately simple SSP variant handling concept
  Import and export of graphical information
    Overall layout information can be transferred via SSP.

## Slide 20: Prototypes: Integration Tool FMI Bench
FMI Bench by PMSF: Workbench for FMUs
  FMU Inspector & Editor, Integration, Automation
  Export Integrated FMUs, Simulators, Remote FMU Execution, FMU-internal Parallelization, IP-Protection
FMI Bench SSP Prototype
  Direct Editing of SSDs, SSPs, incl. Variants
  Generation of Native FMI Bench Projects from SSP Projects
  Generation of FMU or Stand-alone Sim. from SSP
  Parallelization
  IP Protection

## Slide 21: Prototypes – “Co-Simulation Player” (Cybernet)
For Mobile Co-Simulation
  SSP as an Online AP Package
  Flash client and Python server
Natural Interface
  Ring connection geometry
  Flexible 2D/3D Layout
Parameter repository
  Load sqlite.DB as a FMU
  URI online access
Notes: SSP could enlarge the Model Distribution World
over the Internet Web Content Distribution world.
One of the merits of SSP is to facilitate the multi-user collaborations among
multi-domain experts as OEM s and suppliers,
through various environment.
The concept of “Online Co-Simulation Player by Cybernet”
suggests the possibility of SSP format as an Online Simulation Package for
“Anyone, Anytime, Anywhere”
The Cybernet prototype is characterized with the pursuit of Smart User Interface.
This strategy may increase the popularities of SSP Co-Simulations
among younger Engineers who love the Smart device operations.

## Slide 22: Prototypes – TLK MoBA Lab
Focus:
  FMI-based models
  physical connections
  thermodynamic environment
Features
  System Design & Model management
  Simulation & virtual test bench
  Optimization & parameter fitting
Prototype for im-/export support of SSP in development
DaVE
TISC
Excel
SSP

## Slide 23: fMIXer by Modelon
Connect FMUs graphically
Save as .ssp or export to FMU for simulation in any FMI-compliant tool
View FMU information
Manage parameters
Convert ME to CS FMUs
MA-Project “System Structure and Parameterization” – Current Status
– FMI User Meeting, Prague 2017-05-15

## Slide 24: FMI Kit – FMI Library for Simulink
FMI Kit by Dassault Systèmes
Export models as FMUs
Import of FMUs into Models
Initial support of SSP

## Slide 25: SSP support by solidThinking Activate®
Leverage complete FMI 2.0 support (import/export, ME and CS)
Simulation of connected FMUs, with handling of parameters
Support of SSP format for both import and export (WIP)
MA-Project “System Structure and Parameterization” – Current Status
– FMI User Meeting, Prague 2017-05-15